## Slide 1
LEAKWATCH
Machine Learning for Water-Leak Detection, Localization, and Emergency Dispatch
Final Idea & Project Plan - Week 3
Main research question: Can machine learning detect and locate water-pipe leaks from a few pressure sensors, and route the nearest repair crew, using simulated sensor data?
Chirumamilla Sri Ravali
B00120507
Computer Science - Data Science
1

## Slide 2
1. PROJECT IDEA
What I am building and why
What I am building
A machine-learning system, LeakWatch, that reads pressure from a few sensors on a water network. It detects a leak, localizes it (which pipe or area), and dispatches the nearest crew - a full detect-locate-respond pipeline.
Why this problem?
Cities lose 30 to 50 percent of treated water to hidden underground leaks. Oklahoma City had over 1,100 main breaks last year, in old iron pipes and clay soil. Underground leaks are found late.
Main contribution
My own work is the residual feature, the detection and localization models, and the crew-dispatch step. Most leak-detection research stops at 'found it' - the response layer is my addition.
Research question
Can machine learning detect and locate leaks from only a few pressure sensors, and route the nearest crew - using simulated data validated against a real benchmark?
2
Notes: Say what LeakWatch is in one sentence, then why it matters using the Oklahoma numbers. Point to 'Main contribution' - stress this is MY own work on top of standard tools. End by reading the research question.

## Slide 3
2. PROJECT DESCRIPTION
Problem -> Method -> Evaluation
Problem
Only a few sensors watch hundreds of pipes, so a leak must be inferred from limited readings - and caught quickly, before it wastes water and floods roads.
Proposed method
Simulate leaks to build labeled data, turn readings into the residual signal, train a detection model and a localization model, and add a shortest-path dispatch step.
Evaluation
Compare against a simple baseline. Measure detection accuracy, detection delay, localization error, and robustness when sensor noise is added.
The signal: residual
Raw pressure moves with daily demand, so a leak is hard to see. The residual removes that daily pattern, so the leak stands out.
Residual = Expected-normal pressure - Actual pressure
3
Notes: Walk Problem -> Method -> Evaluation left to right. Then explain the residual box: raw pressure moves all day with demand, so I use the difference from normal - that makes the leak clear. This residual is the input to my models.

## Slide 4
3. DEVELOPING ENVIRONMENT
Platform, tools, and the water network
Platform
Google Colab - a free cloud notebook for writing code, training, and running demos. Nothing to install locally.
Tools
Python, with WNTR + EPANET (data), pandas & NumPy (handle data), scikit-learn (models), NetworkX (routing), Matplotlib (charts). Code on GitHub.
The water network
Net3, a standard EPANET benchmark of pipes, junctions, tanks, and pumps. I run it through WNTR and inject leaks.
Development progression
1) Net3 for setup and prototyping 2) many leak scenarios for the main dataset 3) the larger L-Town network and BattLeDIM for realism.
4
Notes: This is my setup. Colab so it runs free with no install. Name the tools and what each is for. Net3 is the practice network now; I move to L-Town and BattLeDIM later. Mention my setup already runs.

## Slide 5
4. INITIAL DESIGN
System architecture and data flow
Simulation (EPANET / WNTR)
Creates the network, injects leaks, and produces the pressure readings - with the true leak location known.
ML models (scikit-learn)
One model answers 'is there a leak?'; a second answers 'which node is it at?' from the pattern of drops.
Dispatch (NetworkX)
Turns the network into a graph and uses shortest-path routing to pick the nearest crew and route.
Data flow
Sensor readings
Residual features
Detect
Localize
Dispatch
Data comes in as sensor readings; the models detect and locate the leak; a shortest-path step routes the nearest crew.
5
Notes: Explain the three parts: the simulation makes the data, the two models detect and locate, and the dispatch step routes the crew. Trace the data-flow row left to right. Note dispatch is shortest-path, not machine learning.

## Slide 6
5. DATA SOURCE & DATA COLLECTION
How the project creates its data
Data source
The primary data source is the EPANET / WNTR simulation - not a fixed real-world dataset. I generate the data by simulating the network and injecting leaks myself, so the true answer is always known.
What becomes the dataset?
Pressure readings at each sensor over time, labeled with leak / no-leak and the leak location, plus the residual features I compute from them.
Data collection flow
Load network
Set leak
Simulate
Record pressures
Label
Repeat
Main fields: timestamp, pressure per sensor, residual per sensor, leak_active (0/1), leak_node, scenario id. Real benchmark: BattLeDIM (Zenodo).
6
Notes: Key point: I generate my own data by simulation because real labeled leak data is not public - and because I place the leaks, I know the true answer, which lets me measure accuracy. Walk the flow. BattLeDIM is the real benchmark I validate on.

## Slide 7
5b. EXAMPLE SENSOR DATA
What the generated data looks like
hour | s101 | s111 | s103 | s125 | s163 | leak
0 | 31.6 | 41.5 | 31.2 | 45.5 | 43.9 | 0
47 | 31.3 | 41.5 | 31.0 | 45.5 | 44.1 | 0
48 | 17.6 | 26.6 | 17.1 | 45.4 | 42.3 | 1
49 | 32.8 | 32.9 | 31.1 | 45.4 | 42.4 | 1
At hour 47 -> 48 the leak starts. The sensors nearest the leak (s101, s111, s103) drop sharply, while the far sensors barely move. That pattern is the leak's fingerprint.
7
Notes: Show this real sample from my own data. Point at hour 47 vs 48 - the near sensors crash while far sensors barely change. That drop pattern is the whole signal my models learn.

## Slide 8
REFERENCES
Official sources used for the plan
WNTR documentation: usepa.github.io/WNTR/
EPANET (U.S. EPA): epa.gov/water-research/epanet
BattLeDIM competition: battledim.ucy.ac.cy/
BattLeDIM dataset (Zenodo): zenodo.org/records/4017659
LeakDB: github.com/KIOS-Research/LeakDB
Oklahoma City water-main breaks: okc.gov / kosu.org
8
Notes: These are the official sources: WNTR and EPANET for the tools and data method, BattLeDIM and LeakDB for the real benchmark and to confirm simulation is the standard method, and the Oklahoma City sources for the real-world problem numbers.